## Slide 1: Modeling & Simulation of a Turbojet Engine for Future Commercial Supersonic Transport Utilizing the DEVS-Suite Framework
By Lucio Ortiz and Robert Blazewicz

## Slide 2: The Future of Supersonic Travel
Image Courtesy of NASA

## Slide 3: Turbojet Performance and Efficiency

## Slide 4: Model Turbojet Components & Stages
System of Systems
Complex, Dynamic
Levels of Abstraction

## Slide 5: Modeling a System of Systems:
What do we need to… Model (and Simulate) Complex System of Systems?
  System Components:
    Functional (Algorithms)
    Independent (Loosely Coupled)
  System Communications
    Interactions between components
    Flow of information
  System Environment
    Realistic Environment
    Environmental Variables
    Couplings between Environment and Components

## Slide 6: Existing Tools
Not Readily Available
Lacking Capability

## Slide 7: (Framework) Questions to be Answered:
Can we utilize the DEVS-Suite Framework to model and simulate our Turbojet Engine for Research and Optimization Development?
What framework components will we need to accomplish this goal?
What will our Experimental Frames look like, and how will they need to interact during simulation?

## Slide 8: M&S Theory

## Slide 9: Levels of System Knowledge
Level | Name | What we know at this Level | Turbojet Simulation
0 | Source | What variables to measure and how to observe them | Thrust Specific Fuel Consumption (TSFC), Specific Thrust output, and Turbojet Efficiencies. Observed through various stages of flight (input Mach #’s), including sustained supersonic speeds.
1 | Data | Data collected from a Source System | Flight data and engine output data from research Comparison of turbojet output measurements with AIAA Simulation Software.
2 | Generative | Means to generate data in a Data System | DEVS Model to recreate engine operation and current and adjusted input flow characteristics.
3 | Structure | Components (at lower levels) coupled together to form a generative system | Turbojet Components Inlet (including Fan) Compressor Combustor Turbine (Afterburner) Nozzle

## Slide 10: Fundamental Systems Problems
Systems Problems | Does source of the data exist? What are we trying to learn about it? | Which level transition is involved? | Turbojet Simulation
Systems Analysis | The system being analyzed may exist or may be planned. In either case we are trying to understand its behavioral characteristics. | Moving from higher to lower levels, e.g., using generative information to generate the data in a data system. | Tubojet engines for supersonic flight exist, utilized in military applications. The first step is to attempt a recreation of these engine characteristics and operations under supersonic flight conditions to observe an initial capability baseline.
Systems Inference | The system exists. We are trying to infer how it works from observations of its behavior. | Moving from lower to higher levels, e.g., having data, finding a means to generate it. | We will next try to understand what affects the behaviors of fuel consumption and thrust output during various supersonic flight regimes by adjusting factor (variables) in our model.
Systems Design | The system being designed does not yet exist in the form that is being contemplated. We are trying to come up with a good design for it. | Moving from lower to higher levels, e.g., having a means to generate observed data, synthesizing it with components taken off the shelf. | Finally, our model will provide insight as to the turbojet engine enhancements that may provide for efficient, low-fuel use, commercial supersonic transport aircraft.

## Slide 11: A Unified Model and Experiment Designs Structure
Model & Simulation Theory
Experimental Framework Design
Model Design
Model & Simulate Experiments

## Slide 12: A Unified Model and Experiment Designs Structure
Model & Simulation Theory
Experimental Framework Design
Model Design
Model & Simulate Experiments

## Slide 13: Model Design Strategy
Considering Abstraction Levels
Initial Strategy for the Design of Turbojet Model:
Design basic model for an “Ideal” Turbojet model.
  3 System Components with communication framework
Enhance basic design to include more components.
Further design to incorporate “Real” Turbojet conditions.
  Isentropic Model, Basic.
  Isentropic Model, Complex.
  Polytropic Model, Advanced and Enhanced.

## Slide 14: Model: System Components
Turbojet Equations –
(Inputs/Outputs & Functions to be Considered for DEVS Framework):

## Slide 15: Example: Diffuser

## Slide 16: A Unified Model and Experiment Designs Structure
Model & Simulation Theory
Experimental Framework Design
Model Design
Model & Simulate Experiments

## Slide 17: Experiment Engine a DEVS Support Infrastructure
Experiment Front Porch
Experiment
Back Porch
Experiment Models
Experiment
Data Recorder

## Slide 18: Experiment Engine a DEVS Support Infrastructure
Experiment Front Porch
Experiment
Back Porch
Experiment Models
Experiment
Data Recorder

## Slide 19: Experiment Engine a DEVS Support Infrastructure
Experiment Front Porch
Experiment
Back Porch
Experiment Models
Experiment
Data Recorder

## Slide 20: Experiment Front Porch the generator
Load a design experiment
Execute the experiment’s design for each of the models.
Manage starting each experimental run with the appropriate design factors.
Experiment Front Porch
Experiment
Back Porch
Experiment Models
Experiment
Data Recorder

## Slide 21: Experiment Front Porch the generator
Load a design experiment
Execute the experiment’s design for each of the models.
Manage starting each experimental run with the appropriate design factors.
Experiment Front Porch
Experiment
Back Porch
Experiment Models
Experiment
Data Recorder
One design experiment for all models
Multiple factors
Each factor may have different number of levels
No fixed number of runs

## Slide 22: Experiment Front Porch the generator
Load a design experiment
Execute the experiment’s design for each of the models.
Manage starting each experimental run with the appropriate design factors.
Experiment Front Porch
Experiment
Back Porch
Experiment Models
Experiment
Data Recorder
List of factors:
"Compressor Pressure Ratio"
variable "pi_c"
Low : 12.2
Med : 15.0
Hi : 17.8
"Afterburner State"
variable "afterburnerOn"
Off : false
On : true

## Slide 23: Experiment Front Porch the generator
Load a design experiment
Execute the experiment’s design for each of the models.
Manage starting each experimental run with the appropriate design factors.
Experiment Front Porch
Experiment
Back Porch
Experiment Models
Experiment
Data Recorder
List of experiment runs:
"--" : ["Low", "Off"]
"O-" : ["Med", "Off"]
"+-" : ["Hi", "Off"]
"-+" : ["Low", "On"]
"O+" : ["Med", "On"]
"++" : ["Hi", "On"]

## Slide 24: Experiment Back Porch the accumulator
Has an experiment run completed?
A model can self-declare that a run is complete.
A model can self-declare that a run has terminated.
Optional user defined method to evaluate run completion state.
Experiment Front Porch
Experiment
Back Porch
Experiment Models
Experiment
Data Recorder

## Slide 25: Experiment Back Porch the accumulator
Has an experiment run completed?
A model can self-declare that a run is complete.
A model can self-declare that a run has terminated.
Optional user defined method to evaluate run completion state.
Experiment Front Porch
Experiment
Back Porch
Experiment Models
Experiment
Data Recorder
Model A
Has the run completed?
Had the run terminated?
Call user method to calculate if the run has completed.
Model B
Has the run completed?
Had the run terminated?
Call user method to calculate if the run has completed.
Model C
Has the run completed?
Had the run terminated?
Call user method to calculate if the run has completed.

## Slide 26: Experiment Data Recorder the transducer
Export design experiment data for each run.
A model can self-declare that intermediate results of a run be exported.
Export model results when a run is completed or terminated.
Text and CSV output
Experiment Front Porch
Experiment
Back Porch
Experiment Models
Experiment
Data Recorder

## Slide 27: Experiment Data Recorder the transducer
Export design experiment data for each run.
A model can self-declare that intermediate results of a run be exported.
Export model results when a run is completed or terminated.
Text and CSV output
Experiment Front Porch
Experiment
Back Porch
Experiment
Data Recorder
"<runs>" : [
{"--" : ["Low", "Off"]},
{"O-" : ["Med", "Off"]},
{"+-" : ["Hi", "Off"]},
{"-+" : ["Low", "On"]},
{"O+" : ["Med", "On"]},
{"++" : ["Hi", "On"]}
]
Experiment Models

## Slide 32: A Unified Model and Experiment Designs Structure
Model & Simulation Theory
Experimental Framework Design
Model Design
Model & Simulate Experiments

## Slide 33: Verification & Validation
Verification: Did we build the product right?
3 Part (Model) Verification
  Hand Calculations
  AIAA Calculations
  DEVS Turbojet Calculations
Validation: Did we build the right product?
  Does it simulate our complex System of Systems?
  Can we use it in the way we want to?

## Slide 34: Verification & Validation: Example Test Case

## Slide 35: Verification
3 Models verified
  Isentropic/Subsonic
  Isentropic/Supersonic
  Polytropic/Supersonic

## Slide 36: DEVS vs. AIAA
Isentropic/Static/Subsonic (BPR=0, AB=Off)
Chart: Turbojet Efficiency
| Thermal Efficiency | Performance Efficiency | Overall Efficiency
DEVS Turbojet | 0.57856 | 0.50847 | 0.29418
AEDSys | 0.5464 | 0.5314 | 0.2904
% Error | 0.058853 | 0.043157 | 0.013006

## Slide 37: DEVS vs. AIAA
Isentropic/Static/Supersonic (BPR=0, AB=ON & Off)
Chart: Turbojet Efficiency
| Thermal - AB Off | Perf. - AB Off | Overall - AB Off | Thermal - AB On | Perf. - AB On | Overall - AB On
DEVS Turbojet | 0.68559 | 0.51198 | 0.35101 | 0.65972 | 0.44794 | 0.29551
AEDSys | 0.6777 | 0.5232 | 0.3546 | 0.6525 | 0.4566 | 0.2979
% Error | 0.011643 | 0.021444 | 0.010127 | 0.011059 | 0.018975 | 0.0080208

## Slide 38: DEVS vs. AIAA
Polytropic/Supersonic
Chart: Turbojet Efficiency
| Thermal - AB Off | Perf. - AB Off | Overall - AB Off | Thermal - AB On | Perf. - AB On | Overall - AB On
DEVS Turbojet | 0.56426 | 0.69504 | 0.35101 | 0.51774 | 0.61727 | 0.31959
AEDSys | 0.5576 | 0.7248 | 0.4041 | 0.5252 | 0.6136 | 0.3222
% Error | 0.011941 | 0.041053 | 0.13138 | 0.014198 | 0.0059797 | 0.0081104

## Slide 39: Validation
Many Experimental Runs Complete
(At least) 3 Models Simultaneously
Over 50 runs at a time with variable alterations
Calibration Feature
Models are Independent of Framework

## Slide 41: Example Data
Chart: Performance Efficiency vs. (pressure) Compression Ratio
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
M=1.0 | 0.59854 | 0.45815 | 0.42126 | 0.40329 | 0.39251 | 0.3853 | 0.38015 | 0.37632 | 0.37338 | 0.37108 | 0.36479 | 0.36261 | 0.36216 | 0.36259 | 0.36354 | 0.36481 | 0.36629 | 0.36792
M=1.5 | 0.60738 | 0.5414 | 0.51912 | 0.50779 | 0.50105 | 0.49669 | 0.49375 | 0.49173 | 0.49034 | 0.48939 | 0.48835 | 0.49017 | 0.49314 | 0.49667 | 0.50051 | 0.50454 | 0.50868 | 0.5129
M=1.8 | 0.62874 | 0.58357 | 0.56792 | 0.56026 | 0.55601 | 0.55357 | 0.55219 | 0.55149 | 0.55127 | 0.55137 | 0.55458 | 0.55977 | 0.56571 | 0.57199 | 0.57843 | 0.58499 | 0.59161 | 0.59829
M=2.0 | 0.64557 | 0.61031 | 0.59841 | 0.593 | 0.59038 | 0.58922 | 0.58892 | 0.58917 | 0.58979 | 0.59067 | 0.5971 | 0.60497 | 0.61333 | 0.6219 | 0.63058 | 0.63933 | 0.64816 | 0.65708

## Slide 42: Example Data
Chart: Specific Thrust vs. (pressure) Compression Ratio
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
M=1 | 54.1588 | 82.8164 | 93.8018 | 99.8707 | 103.7532 | 106.4438 | 108.4033 | 109.8781 | 111.0133 | 111.9006 | 114.2227 | 114.8432 | 114.7402 | 114.2714 | 113.5989 | 112.8061 | 111.94 | 111.0286
M=1.5 | 71.7177 | 88.8136 | 95.5017 | 99.0489 | 101.1763 | 102.5296 | 103.4114 | 103.9841 | 104.3432 | 104.5488 | 104.3162 | 103.1426 | 101.6277 | 99.9761 | 98.273 | 96.5579 | 94.8502 | 93.1596
M=1.8 | 77.7992 | 90.1822 | 94.7733 | 96.9942 | 98.1542 | 98.7448 | 98.9952 | 99.0274 | 98.9126 | 98.6949 | 96.8165 | 94.4284 | 91.9221 | 89.4152 | 86.9481 | 84.5338 | 82.1752 | 79.8704
M=2.0 | 80.3204 | 90.101 | 93.4429 | 94.8433 | 95.3892 | 95.4861 | 95.3213 | 94.9934 | 94.5592 | 94.0534 | 91.0285 | 87.7672 | 84.5309 | 81.3816 | 78.3303 | 75.3729 | 72.5008 | 69.7044

## Slide 43: Continuing Work with DEVS-Framework

## Slide 44: Full Flight Regime: Sample Test Flight

## Slide 45: Tomorrow… and Beyond!

## Slide 46: Questions?

## Slide 47: Experiment Engine a Development Plan
Lofty vision
Elaborate project plan for the Turbojet Engine
Our project plan was like a traditional startup business plan. A solution for a fictitious customer that quickly dies as soon as the product receives actual customer feedback.
10-weeks to develop project
Defining the experiment engine took about 3-weeks leaving 6-weeks to reach a near final implementation.
  Lot of pressure to develop a useful tool for both the Turbojet Engine and the general DEVS Suite.
  Lots of uncertainty with the design path, and significant upfront chaos.
Our approach:
  Lean development process to develop a minimal viable product.
  Rapid incremental prototyping based on customer feedback.
    Customers: Lucio Ortiz and Professor Sarjoughian
  Use of Lean methodology
  Goal and milestones structured within 2-week Scrum sprints

## Slide 48: Experiment Engine a Development Plan
Sprint Board

## Slide 49: Experiment Engine a Development Plan
Microsoft Project

## Slide 50: M&S/Design of Experiments
A Systematic, Flexible, and Repeatable Process

## Slide 51: R&D Problem
What effect does the pressure compression ratio in the compressor stage have on the performance of the turbojet engine, during long-duration, supersonic flight?
Can we eliminate the use of a Hi-Bypass (ratio) fan, in exchange for either a Low-Bypass (ratio) or (straight) turbojet engine, for additional propulsion, and still meet thrust and fuel requirements for long-duration supersonic flight? (without the use of afterburner)
What effect does decreasing the limitations/constraints of the Turbine Inlet temperature offer for the turbojet performance during long-duration supersonic flight? (i.e. Increasing the allowable temperature by use of new, high tolerance materials or designs)
If the above parameters show a significant effect on the turbojet performance, is there a combination of pressure compression ratio, (low) by-pass ratio, and turbine inlet temperature that would optimize turbojet performance during long-duration, supersonic flight?
(Initial Model) Questions to be Answered:

## Slide 52: Ambitious (Optional) Questions:
Is there any insight as to what may be necessary to re-design a turbojet engine to allow the extraction of a significant amount of (auxiliary) power, for use in hi-power payload packages?
Can we predict what properties a fuel might need to have in order to offer an existing turbojet design, significantly more thrust than traditional jet fuel?

## Slide 53: Design of Experiments
Initial Design of Experiments:
Phase I – Initialization, Verification & Validation of Model
Simulate “Ideal” Turbojet model with all static input values for a baseline verification and validation of basic model.
Simulate “Ideal” Turbojet model with various levels of pressure compression ratio for verification and validation of changing variable experimentation.
Simulate “Ideal” Turbojet model with afterburner, static input values.
Simulate “Ideal” Turbojet model with by-pass ratio fan, static input values.
Simulate “Real” Turbojet model with afterburner and by-pass ratio fan, static values.
Phase I

## Slide 54: Design of Experiments
Phase II – Design of Experiments for Analysis
Fractional Factorial Experiment:
4 Factors
  Pressure Compression Ratio
  By Pass Ratio (BPR)
  Turbine Inlet Temperature
  Afterburner
2 Levels, (Each Factor)
  Pressure Compression Ratio (Low, Hi)
  BPR (Low, Hi)
  Turbine Inlet Temperature (Low, Hi)
  Afterburner (On, Off)
Phase II

## Slide 55: Design of Experiments: Phase II: Fractional Factorial
Randomized Model with Replicate
Turbojet Experiment Set 01: 16 runs |  |  |  |  |  |  |  |  |  | 
Column1 | pi_c | alpha | Tt4 | Afterburner | eta_o | eta_p | eta_t | F | F_s | TSFC
1 | 24.25 | 1 | 2400 | ON |  |  |  |  |  | 
2 | 13.5 | 1 | 3600 | OFF |  |  |  |  |  | 
3 | 24.25 | 0 | 2400 | OFF |  |  |  |  |  | 
4 | 13.5 | 2 | 1200 | OFF |  |  |  |  |  | 
5 | 13.5 | 0 | 3600 | ON |  |  |  |  |  | 
6 | 24.25 | 2 | 2400 | OFF |  |  |  |  |  | 
7 | 13.5 | 2 | 3600 | ON |  |  |  |  |  | 
8 | 35 | 2 | 3600 | OFF |  |  |  |  |  | 
9 | 24.25 | 2 | 1200 | ON |  |  |  |  |  | 
10 | 35 | 1 | 1200 | OFF |  |  |  |  |  | 
11 | 13.5 | 0 | 1200 | OFF |  |  |  |  |  | 
12 | 13.5 | 1 | 1848 | ON |  |  |  |  |  | 
13 | 35 | 2 | 2400 | ON |  |  |  |  |  | 
14 | 35 | 0 | 1200 | ON |  |  |  |  |  | 
15 | 27.045 | 1 | 3600 | ON |  |  |  |  |  | 
16 | 35 | 0 | 3600 | OFF |  |  |  |  |  | 

## Slide 56: Design of Experiments
(Possible) Phase III – Design of Experiments for Optimization
Based on findings from Phase II:
Are there optimal levels of the variables which offer the greatest potential of performance enhancement?
Creation of Randomized ‘Optimal’ Design of Experiments with continuous levels for factor variables
Phase II

## Slide 57: Design of Experiments: Fractional Factorial Results
Turbojet Experiment Set 01: 16 runs |  |  |  |  |  |  |  |  |  | 
Column1 | pi_c | alpha | Tt4 | Afterburner | eta_o | eta_p | eta_t | F | F_s | TSFC
1 | 24.25 | 1 | 2400 | ON | 0.23 | 0.70 | 0.32 | 6368.69 | 37.46 | 2.93
2 | 13.5 | 1 | 3600 | OFF | 0.41 | 0.67 | 0.60 | 9219.11 | 54.23 | 1.17
3 | 24.25 | 0 | 2400 | OFF | 0.34 | 0.82 | 0.42 | 5151.46 | 30.30 | 1.35
4 | 13.5 | 2 | 1200 | OFF | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
5 | 13.5 | 0 | 3600 | ON | 0.28 | 0.52 | 0.54 | 21703.27 | 127.67 | 1.72
6 | 24.25 | 2 | 2400 | OFF | 0.23 | 0.44 | 0.53 | 1524.03 | 8.96 | 1.52
7 | 13.5 | 2 | 3600 | ON | 0.37 | 0.63 | 0.58 | 9508.49 | 55.93 | 1.31
8 | 35 | 2 | 3600 | OFF | 0.51 | 0.78 | 0.65 | 6059.31 | 35.64 | 0.92
9 | 24.25 | 2 | 1200 | ON | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
10 | 35 | 1 | 1200 | OFF | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
11 | 13.5 | 0 | 1200 | OFF | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
12 | 13.5 | 1 | 1848 | ON | 0.14 | 0.83 | 0.17 | 5728.87 | 33.70 | 3.25
13 | 35 | 2 | 2400 | ON | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
14 | 35 | 0 | 1200 | ON | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
15 | 27.045 | 1 | 3600 | ON | 0.33 | 0.57 | 0.57 | 12727.58 | 74.87 | 1.46
16 | 35 | 0 | 3600 | OFF | 0.38 | 0.63 | 0.60 | 13316.15 | 78.33 | 1.26

## Slide 58: Effect Summary
JMP Effect Screening

## Slide 59: Effect Summary
Optimization:
Maximize Desireability:
Max Efficiency
Max Thrust
Minimize Fuel Flow

## Slide 60: Factor Insight
What are the behaviors over the span of operation?
Chart: Specific Thrust vs. (pressure) Compression Ratio
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
M=1 | 54.1588 | 82.8164 | 93.8018 | 99.8707 | 103.7532 | 106.4438 | 108.4033 | 109.8781 | 111.0133 | 111.9006 | 114.2227 | 114.8432 | 114.7402 | 114.2714 | 113.5989 | 112.8061 | 111.94 | 111.0286
M=1.5 | 71.7177 | 88.8136 | 95.5017 | 99.0489 | 101.1763 | 102.5296 | 103.4114 | 103.9841 | 104.3432 | 104.5488 | 104.3162 | 103.1426 | 101.6277 | 99.9761 | 98.273 | 96.5579 | 94.8502 | 93.1596
M=1.8 | 77.7992 | 90.1822 | 94.7733 | 96.9942 | 98.1542 | 98.7448 | 98.9952 | 99.0274 | 98.9126 | 98.6949 | 96.8165 | 94.4284 | 91.9221 | 89.4152 | 86.9481 | 84.5338 | 82.1752 | 79.8704
M=2.0 | 80.3204 | 90.101 | 93.4429 | 94.8433 | 95.3892 | 95.4861 | 95.3213 | 94.9934 | 94.5592 | 94.0534 | 91.0285 | 87.7672 | 84.5309 | 81.3816 | 78.3303 | 75.3729 | 72.5008 | 69.7044

## Slide 61: Factor Insight
What are the behaviors over the span of operation?
Chart: TSFC vs. (pressure) Compression Ratio
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
M=1 | 3.4014 | 2.1546 | 1.8594 | 1.7146 | 1.6246 | 1.5617 | 1.5142 | 1.4768 | 1.4461 | 1.4203 | 1.3328 | 1.2794 | 1.2416 | 1.2127 | 1.1894 | 1.1699 | 1.1532 | 1.1385
M=1.5 | 2.5004 | 1.9405 | 1.7538 | 1.6521 | 1.5854 | 1.537 | 1.4996 | 1.4695 | 1.4444 | 1.423 | 1.3486 | 1.3018 | 1.2681 | 1.2421 | 1.221 | 1.2034 | 1.1883 | 1.1752
M=1.8 | 2.2552 | 1.8575 | 1.7093 | 1.6251 | 1.5685 | 1.5267 | 1.4939 | 1.4673 | 1.445 | 1.4258 | 1.3585 | 1.3157 | 1.2849 | 1.2613 | 1.2423 | 1.2267 | 1.2137 | 1.2028
M=2.0 | 2.1474 | 1.8181 | 1.6885 | 1.6133 | 1.562 | 1.5238 | 1.4937 | 1.469 | 1.4483 | 1.4305 | 1.3677 | 1.3279 | 1.2996 | 1.2782 | 1.2616 | 1.2486 | 1.2384 | 1.2305

## Slide 62: Factor Insight
What are the behaviors over the span of operation?
Chart: Performance Efficiency vs. (pressure) Compression Ratio
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
M=1.0 | 0.59854 | 0.45815 | 0.42126 | 0.40329 | 0.39251 | 0.3853 | 0.38015 | 0.37632 | 0.37338 | 0.37108 | 0.36479 | 0.36261 | 0.36216 | 0.36259 | 0.36354 | 0.36481 | 0.36629 | 0.36792
M=1.5 | 0.60738 | 0.5414 | 0.51912 | 0.50779 | 0.50105 | 0.49669 | 0.49375 | 0.49173 | 0.49034 | 0.48939 | 0.48835 | 0.49017 | 0.49314 | 0.49667 | 0.50051 | 0.50454 | 0.50868 | 0.5129
M=1.8 | 0.62874 | 0.58357 | 0.56792 | 0.56026 | 0.55601 | 0.55357 | 0.55219 | 0.55149 | 0.55127 | 0.55137 | 0.55458 | 0.55977 | 0.56571 | 0.57199 | 0.57843 | 0.58499 | 0.59161 | 0.59829
M=2.0 | 0.64557 | 0.61031 | 0.59841 | 0.593 | 0.59038 | 0.58922 | 0.58892 | 0.58917 | 0.58979 | 0.59067 | 0.5971 | 0.60497 | 0.61333 | 0.6219 | 0.63058 | 0.63933 | 0.64816 | 0.65708

## Slide 63: Factor Insight
What are the behaviors over the span of operation?
Chart: Thermal Efficiency vs. (pressure) Compression Ratio
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
M=1.0 | 0.10267 | 0.23302 | 0.29844 | 0.34045 | 0.37066 | 0.39386 | 0.41246 | 0.42784 | 0.44086 | 0.45206 | 0.49142 | 0.51576 | 0.53258 | 0.54496 | 0.55444 | 0.56189 | 0.56786 | 0.57269
M=1.5 | 0.22549 | 0.33493 | 0.38944 | 0.42421 | 0.44903 | 0.46797 | 0.48304 | 0.49542 | 0.50581 | 0.5147 | 0.54519 | 0.56317 | 0.57489 | 0.58291 | 0.58851 | 0.59239 | 0.59501 | 0.59665
M=1.8 | 0.29506 | 0.39218 | 0.44018 | 0.47057 | 0.49209 | 0.50838 | 0.52124 | 0.5317 | 0.54041 | 0.54777 | 0.57226 | 0.58566 | 0.59348 | 0.59798 | 0.60026 | 0.60094 | 0.60041 | 0.5989
M=2.0 | 0.33781 | 0.42709 | 0.4709 | 0.49842 | 0.51776 | 0.53227 | 0.54362 | 0.55277 | 0.5603 | 0.56659 | 0.58669 | 0.59653 | 0.60116 | 0.60262 | 0.6019 | 0.59957 | 0.59594 | 0.59122

## Slide 64: Factor Insight
Similarly for other Factors
Chart: Specific Thrust vs. Turbine Inlet Temperature
| 3000 | 3600 | 3800 | 4200
M=1.0 | 91.1247 | 113.5989 | 120.5075 | 133.6835
M=1.5 | 73.9975 | 98.273 | 105.6683 | 119.7102
M=1.8 | 61.2255 | 86.9481 | 94.7128 | 109.3919
M=2.0 | 51.4269 | 78.3303 | 86.3832 | 101.5482

## Slide 65: Configuration Support via Calibration & Value Management
Model Calibration
Experiment Front Porch
Experiment
Back Porch
Value Management
Experiment Models
Experiment
Data Recorder

## Slide 66: Model Calibration
Redefine model constants at runtime.
Each experiment model has it’s own calibration settings.
High level external control of parameters that define a model.
Experiment Front Porch
Experiment
Back Porch
Value Management
Experiment
Data Recorder
Class constants:
  KeTJET_DDa_VelocityJerk
  ^^^
  second derivative of acceleration
Model Calibration

## Slide 67: Model Calibration
Redefine model constants at runtime.
Each experiment model has it’s own calibration settings.
High level external control of parameters that define a model.
Experiment Front Porch
Experiment
Back Porch
Value Management
Experiment
Data Recorder
Class constants:
  KeTJET_DDa_VelocityJerk
  ^^^
  second derivative of acceleration
K[e|a][A-Z0-1]+_<type>_<name>
  K : calibration variable e|a : element or array part : component name acronym type : a defined type name : variable name
Model Calibration

## Slide 68: Model Calibration
Redefine model constants at runtime.
Each experiment model has it’s own calibration settings.
High level external control of parameters that define a model.
Experiment Front Porch
Experiment
Back Porch
Value Management
Experiment
Data Recorder
Class constants:
  KeTJET_DDa_VelocityJerk
  ^^^
  second derivative of acceleration
Type definitions:
  boolean : "Bool" char : byte : short : int : "Cnt", "ms" long : float : double : "a", "Da", "DDa" String : "Str"
Model Calibration

## Slide 69: Model Calibration
Redefine model constants at runtime.
Each experiment model has it’s own calibration settings.
High level external control of parameters that define a model.
Experiment Front Porch
Experiment
Back Porch
Value Management
Experiment
Data Recorder
Class constants:
  KeTJET_DDa_VelocityJerk
  ^^^
  second derivative of acceleration
"KeTJET_DDa_VelocityJerk" : "0.35"
"KeTJET_Bool_Afterburner" : "false"
"KeTJET_Cnt_SimViewRows" : "2"
"KeTJET_Str_FluidModel" : "Isentropic/Static (subsonic)"
Model Calibration

## Slide 70: Value Management
An efficient way to manipulate model values.
Experiment Front Porch
Experiment
Back Porch
Experiment
Data Recorder
Value Management
Your model class:
Define initial values externally
Declare class variables
Code focuses on using values rather than packing / unpacking values from modeling link structure
Value Management

## Slide 71: Value Management
An efficient way to manipulate model values.
Experiment Front Porch
Experiment
Back Porch
Experiment
Data Recorder
Value Management
Define initial value externally
"Tzero" : "double", "411.8", "[degR]", "Inlet temperature" "gamma" : "double", "1.4", "[Cp/Cv]", "Specific Heat Ratio of air " "Rair" : "double", "53.35", "[ft-lb/degR-lbm]", "Specific gas cnst. dry air" "gc" : "double", "32.174", "[lbm-ft/s^2]", "gravity cnst"
Value Management

## Slide 72: Value Management
An efficient way to manipulate model values.
Experiment Front Porch
Experiment
Back Porch
Experiment
Data Recorder
Value Management
Declare class variables
/* Inputs */ private double Tzero; private double gamma; private double Rair; private double gc; /* Outputs */ private double azero;
Value Management

## Slide 73: Value Management
An efficient way to manipulate model values.
Experiment Front Porch
Experiment
Back Porch
Experiment
Data Recorder
Value Management
Code focus
public void process(final ValueSet valueSet) { valueSet.valuePop(this); // [ft/s] speed of sound azero = Math.sqrt(gamma*Rair*gc*Tzero); if (valueSet.isFirstPass()) valueSet.addValue(name, "azero", Value.theType.eDouble, azero, "[ft/s]", "Speed of sound"); valueSet.valuePush(this); }
Value Management

## Slide 76: DEVS vs. AIAA
Chart: Specific Thrust
| Specific Thrust
DEVS Turbojet | 47.8226
AEDSys | 43.47
% Error | 0.10013
Isentropic/Static/Subsonic (BPR=0, AB=Off)

## Slide 77: DEVS vs. AIAA
Isentropic/Static/Subsonic (BPR=0, AB=Off)
Chart: TSFC
| TSFC
DEVS Turbojet | 0.69731
AEDSys | 0.7125
% Error | 0.02132

## Slide 78: DEVS vs. AIAA
Polytropic/Supersonic
Chart: Specific Thrust
| Specific Thrust - AB Off | Specific Thrust - AB On
DEVS Turbojet | 55.4085 | 76.0604
AEDSys | 55.493 | 90.57
% Error | 0.0015229 | 0.1602

## Slide 79: DEVS vs. AIAA
Polytropic/Supersonic
Chart: TSFC
| TSFC - AB Off | TSFC - AB On
DEVS Turbojet | 1.2123 | 1.5008
AEDSys | 1.2104 | 1.5144
% Error | 0.0015597 | 0.0089941